## Slide 1
Manufacturing
Downtime Analysis
Data-driven maintenance intelligence for industrial operations
Final Project | Team 1 | Supervised by Dr. Amal Mahmoud

## Slide 2
Our Team
Supervised by
Dr. Amal Mahmoud
Ahmed Yasser
01555804012
linkedin.com/in/ahmedyassermousa
Mohamed El-Nady
01152455483
linkedin.com/in/mohamed--el-nady
Mohamed Adel
Abdulrahman Mohamed
01551474804
linkedin.com/in/abdulrahman-salahuddin

## Slide 3
Agenda
01
Introduction to Data
Dataset overview, structure & objectives
02
Data Cleaning
Validation, outliers & reliability
03
Data Modeling
Star schema & dimensional design
04
KPIs
OEE, Availability, Performance, Quality
05
Dashboard
Interactive management-level visuals
06
Insights & Findings
Key takeaways from the analysis

## Slide 4
Introduction to Data
Definition
Real industrial machine operation data from a multi-machine manufacturing environment.
Data Structure
Time-based operational records with multiple machines running simultaneously.
Analysis Objectives
Measure operational efficiency across all machines
Calculate manufacturing KPIs (OEE, Availability, Quality)
Build a management-level dashboard for decision support
Enable proactive maintenance: Preventive & Predictive
Identify root causes of downtime and failure events
10,000
Records
20
Machines
4
Machine Types
4
Brands
12
Months

## Slide 5
Maintenance Types
01
Preventive
Scheduled maintenance based on time or usage intervals
Performed before failure occurs
Reduces unexpected downtime
Planned resource allocation
Lower cost per intervention
02
Predictive
Data-driven maintenance based on real-time machine condition
Uses sensor data & machine signals
Predicts failures before they occur
Minimizes unnecessary maintenance
Optimal cost & uptime balance
03
Corrective
Performed after a failure has already occurred
Reactive — triggered by breakdown
Restores equipment to normal
Highest cost per event ($633 avg)
Causes unplanned downtime

## Slide 6
Data Cleaning
Ensuring data reliability before analysis
1
Missing Values
Distinguished missing from zero values. Verified all null fields and their context before handling.
2
Outlier Detection
Checked for extreme RPM values (too low or too high). Applied domain logic rather than pure statistics.
3
Logical Constraints
Enforced: Production units ≥ 0, Downtime ≥ 0, Failures aligned with downtime hours.
4
Data Preservation
No aggressive removal — preserved realistic operational behavior including rare but valid edge cases.
Result: Clean, validated dataset ready for accurate KPI calculation and dimensional modeling

## Slide 7
Data Modeling
Step 1: Business Questions
Every great data model starts by answering the right business questions.
Who?
Machine Dimension
→ Machine ID, type (LATHE, CNC, PRESS, CONVEYOR), brand
What?
Product Dimension
→ Product ID, product type (L, M, H quality grades)
When?
Time Dimension
→ Date, hour, day, month for trend & seasonality analysis
Why?
Failure & Maintenance
→ Failure type, maintenance type and cost impact

## Slide 8
Data Modeling
Step 2: Star Schema Design
FACT TABLE
Operating Hours Downtime Hours Production Units Failure Events Maintenance Cost
DimMachine
machine_key
Machine_ID, Type, Brand
DimProduct
product_key
Product_ID, Type (L/M/H)
DimTime
date_key
Date, Hour, Day, Month
DimFailure
failure_key
Failure Type, Code
DimMaintenance
maint_key
Type, Cost, Duration

## Slide 9
Key Performance Indicators
Five metrics that define manufacturing excellence
A
Availability
(Op. Time − Downtime) ÷ Op. Time
Machine uptime readiness
P
Performance
Actual Output ÷ Theoretical Output
Speed vs maximum capability
Q
Quality
Good Units ÷ Total Units Produced
Defect-free production rate
OEE
Overall Equipment Effectiveness
Availability × Performance × Quality
Combined efficiency score
M
Maintenance KPIs
MTBF | MTTR | Cost/Failure
Reliability & repair speed

## Slide 10
KPIs: Availability & Performance
A
Availability
Measures machine readiness and uptime
Formula
(Operating Time − Downtime) ÷ Operating Time
Purpose
Identify losses caused by breakdowns and maintenance
Insight
High availability = stable machine reliability. Low availability signals frequent breakdowns or excessive maintenance windows.
P
Performance
Measures speed vs. maximum capability
Formula
Actual Output ÷ Theoretical Output
Purpose
Detect slow-running and speed losses in production
Insight
Low performance is the #1 OEE loss driver in this dataset — machines are running below their maximum RPM capacity.

## Slide 11
KPIs: Quality & OEE
Q
Quality
Measures production quality efficiency
Formula
Good Units ÷ Total Units Produced
Purpose
Identify losses caused by defects and rework
Insight
Quality levels are very high in this dataset — showing stable production. This is NOT the primary efficiency loss driver.
OEE
Overall Equipment Effectiveness
The single most important manufacturing metric
Formula
Availability × Performance × Quality
Purpose
Provide one comprehensive efficiency indicator
Insight
Main insight: Performance is the weakest OEE component. Optimizing machine speed has the highest improvement potential.

## Slide 12
KPIs: Maintenance Metrics
MTBF
Mean Time Between Failures
Formula
Total Operating Time ÷ Number of Failures
Definition
Average operating time between failure events
Higher MTBF = more reliable machines. Benchmark against manufacturer specs to detect degradation early.
MTTR
Mean Time To Repair
Formula
Total Repair Time ÷ Number of Repairs
Definition
Average time required to restore equipment to operation
Lower MTTR = faster recovery. Key metric for maintenance team efficiency and spare parts availability.
CPF
Cost Per Failure
Formula
Total Maintenance Cost ÷ Number of Failures
Definition
Average cost incurred per failure event
Dataset finding: Corrective failures cost $633 avg vs $175 preventive — a 3.6× difference per event.

## Slide 13
Dashboard
Ready?
Live demonstration follows

## Slide 14
Key Insights
3.4%
Overall failure rate
339 of 10,000 records
3.6×
Corrective vs preventive cost
$633 avg vs $175 avg
11.4%
July failure rate spike
vs 2% annual average
94.4%
Flag-triggered failure rate
Any 1 flag = near-certain failure
Performance is the #1 OEE loss driver — machines run below maximum speed, not because of breakdowns or quality failures.
June–July seasonal spike: failure rates jump to 9% and 11.4%. Schedule proactive inspections before summer every year.
LATHE machines have the highest failure rate (3.7%) and most downtime. CNC is second. PRESS machines are the most reliable.
Tool wear >200 min drives 15.5% failure rate (vs 2.2% below 150 min). Replace tools before the 200-minute threshold.

## Slide 15
Thank You
for your attention
Manufacturing Downtime Analysis | Final Project | Team 1 | Supervised by Dr. Amal Mahmoud